## Slide 1: DCA Members' Forum 2025
Rock Drilling
Mud-Motor versus Dual-Rod-System

## Slide 2: Daily schedule
09:00 – 09:15 Welcome and Introduction
09:15 – 10:30 Workshop Session 1
10:30 – 11:00 Coffee break
11:00 – 12:30 Workshop Session 2
12:30 – 13:30 Lunch break
13:30 – 14:45 Workshop Session 3
14:45 – 15:15 Coffee break
15:15 – 16:30 Workshop Session 4
16:30 – 17:00 Final discussion

## Slide 3: Welcome and Introduction
Brief introduction of the experts and the participants
Character of the Forum / Workshop
  No classic lecture and no classic presentation Exchange of thoughts and opinions Discussions Joint development of results and conclusions
Why this topic?
Today's goals and expectations

## Slide 4: Agenda
Session 1 History, technical structure, modes of action
History, BHA structure, mode of operation, deployed HDD-systems, ROPs, controllability, areas of application/application limits, (drilling lengths, radii, subsoil), equipment costs
Session 2 Measurement Methods/Positioning Methods in Comparison Walk-Over vs. Wire-Line, Wire-Line with Dual-Rod?, Accuracies, areas of application/limits of the measuring/locating methods, time required, costs
Session 3 Drilling fluid and borehole hydraulics
Fluid requirements, pump requirements, environmental aspects, Borehole cleaning, mud pressures, mud outbreaks, Borehole cleaning, costs for drilling fluid and wear and tear of the tools
Session 4 Comparison table/differentiation matrix and project examples
Comparison table/differentiation matrix, project examples

## Slide 5: Session 1 – History, technical structure, modes of action
Brief history of the Mud-Motors and Dual-Rod-Systems
Technical Setup of systems and dimensions
HDD-systems used
Modes of action and power transmission (torque, speed, flow rates)
Rate of penetration
Controllability
Areas of application/application limits (drilling lengths, drilling radius, subsoil/geology, drag pipes)
Equipment costs incl. inspection and wear (also rods)

## Slide 6: Session 1 – History, technical structure, modes of action
Brief history of the (drilling)Mud-Motors and Dual-Rod-Systems
Mud-Motors
  In 1932, Moineau developed the positive displacement pump with stator and rotor End of the 1960s used in deep drilling technology In the 1980 standard tools in directional drilling for Oil & Gas Mud-Motors in HDD since 1980
Dual-Rod-Systems
  First HDD-rig-manufacturer Ditch Witch, Mid-1990s
  Other manufacturers are developing Dual-Rod-Systems
  Dominant in rock drilling with drilling rigs with a pull-force of up to 30 t
  Meanwhile also for drilling rigs with a pull- force of up to 60 t

## Slide 7: Session 1 – History, technical structure, modes of action
Technical design of the systems and dimensions
Mud-Motors
Quelle:
H.-J. Bayer, HDD-Praxis Handbuch
Quelle:
H.-J. Bayer, HDD-Praxis Handbuch

## Slide 8: Session 1 – History, technical structure, modes of action
Mud-Motors
Quelle:
Prime Horizontal
Technical design of the systems and dimensions

## Slide 9: Session 1 – History, technical structure, modes of action
Technical design of the systems and dimensions
Mud-Motors (here in combination with rockbreaker unit)
Quelle:
Tracto-Technik
Quelle:
Tracto

## Slide 10: Session 1 – History, technical structure, modes of action
Quelle:
Tracto-Technik
Technical design of the systems and dimensions
Mud-Motors
Comparison of the distance between the drill head and the transmitter at
  Mudmotor Standard 3-¾“
      Mudmotor in combination with Rockbreaker 3-3/4"

## Slide 11: Session 1 – History, technical structure, modes of action
Technical design of the systems and dimensions
Dual-Rod-Systems
Drive of the bit via internal drill pipe
Dual-Rod-System / Double-Rod-System
Quelle:
H.-J. Bayer, Tracto Technik

## Slide 12: Session 1 – History, technical structure, modes of action
Technical design of the systems and dimensions
Dual-Rod-System
Housing
Sender / Transmitter
Rockmaster
Quelle:
Borestore.com/Vermeer

## Slide 13: Session 1 – History, technical structure, modes of action
Deployed HDD-Systems
with Dual-Rod-System
mini, midi, and "small" maxi rigs from different manufacturers
  with 12 t, 18 t, 30 t, 54 t max. pull force
with Mud-Motors
midi, maxi and mega rigs from various manufacturers
  with 15 t, 18 t, 28 t, 30 t, 45 t, 60 t to 600 t max. pull force
In this forum, we want to compare the systems for HDD-systems from 18 t – 54 t !!

## Slide 14: Session 1 – History, technical structure, modes of action
Modes of action and power transmission (torque, speed, flow rates)
Mud-Motors (for 18t-54t Rigs)
Power transmission by converting hydraulic energy into mechanical energy
Torques: 500-3.000 Nm
Speeds: 100-250 1/min
Flow: 250-1.000 l/min
(for pilot drilling)
Quelle:
H.-J. Bayer, HDD-Praxis Handbuch

## Slide 15: Session 1 – History, technical structure, modes of action
Mud-Motors
Relationship between torque/speed according to the number of gears of the motors
Quelle:
"Flachbohrtechnik" von Werner Arnold
Modes of action and power transmission (torque, speed, flow rates)

## Slide 16: Session 1 – History, technical structure, modes of action
Modes of action and power transmission (torque, speed, flow rates)
Dual-Rod-System
(for 18t-54t Rigs)
Power transmission through internal linkage
Torques: 1.200-3.000 Nm
Speeds: 50-350 1/min
Flow: 60-150 l/min
(for pilot drilling)
Quelle:
H.-J. Bayer, Tracto Technik

## Slide 17: Session 1 – History, technical structure, modes of action
Rate of penetration
Are there differences between the two systems (possibly due to different torques, speeds and contact pressures)?
Dual-Rod-Systems
Mud-Motors
No significant difference !!
Or ???

## Slide 18: Session 1 – History, technical structure, modes of action
Controllability
Factors influencing controllability:
  Geology Geometry and dimensions Bent Sub Rigidity/Stiffness of the system
What exactly is meant by controllability? Discussion
Are there differences in controllability here? Discussion
Dual-Rod-Systems
Mud-Motors
What differences?

## Slide 19: Session 1 – History, technical structure, modes of action
Areas of application/limits of application (drilling lengths, drilling radius, subsoil/geology, string behind reamer)
Drilling lengths
What factors have a significant influence on the possible drill lengths?
  Drilling rig used Power Transmission and Losses per System Possible Pumping Rates for Mud-Motors
Dual-Rod-Systems (18 t, 30 t, 54 t class)
Drilling lengths approx.: 200-300 m (18 t) 300-400 m (30 t) 400-600 m (54 t), or more??
Subsoil (geology): Rock, inhomogeneous ground
Mud-Motors (18 t, 30 t, 54 t class)
Drilling lengths approx.: 200-350 m (18 t) 300-450 m (30 t) 400-650 m (54 t), or more??
Subsoil (geology): Rock, inhomogeneous ground

## Slide 20: Session 1 – History, technical structure, modes of action
Dual-Rod-Systems
(under optimal conditions)
  18 t Class 50 m
  30 t Class 65 m
  54 t Class 65 m
Mud-Motors
(under optimal conditions)
  18 t Class 100 m (3 3/4 75 m with Rockbreaker)
  30 t Class 100 m
  54 t Class 100 m
Areas of application/application limits (drilling lengths, drilling radius, subsoil/geology, drag pipes)
Possible drill radii
What factors have a significant influence on the minimum drill radii?
  Geology Geometry and dimensions (including bits) Bent Sub Stiffnes of the system

## Slide 21: Session 1 – History, technical structure, modes of action
Factors for drillability in hard-soft alternation in rock:
Mud Flow
RPM (rotations per minute)
ROP (rate of penetration, Speed)
Steerability
Reaction-/Correction time
Quelle (alle Bilder):
H.-J. Bayer u. M. Reich , HDD -Felsbohrtechnik
Areas of application/limits of application (subsoil/geology) for Dual-Rod-Systems

## Slide 22: Session 1 – History, technical structure, modes of action
Areas of application/application limits (drilling lengths, drilling radius, subsoil/geology, drag pipes)
Use of drill pipe behind reamer
  Dual-Rod-Systems
  Mud-Motors
very time-consuming, but possible
Easy

## Slide 23: Session 1 – History, technical structure, modes of action
Equipment costs incl. inspection and wear (also drill pipe)
Dual-Rod-Systems
Purchase price: approx. 9,000 -14,000 EUR for the Rockmaster (without bit)
Inspection: approx. 1,000-2,000 EUR every 100 operating hours
Wear: rather high, because less or incorrect drilling fluid is pumped ??
Costs of rods: rather high in comparison (inner and outer drill pipe)
Mud-Motors
Purchase price: approx. 25,000 EUR 3 3/4 inches, 30.000 EUR 4 3/4 inches approx. 40,000 EUR 6 3/4 inches (without bit) (Often rental)
Inspection: approx. 2,000-2,400 EUR every 150 operating hours
Wear: rather low, because significantly more drilling fluid is pumped
Costs of rods: rather low in comparison

## Slide 24: Session 2 – Measurement Methods/Positioning Methods in Comparison
Locating technology Walk-Over for Dual-Rod-System
Locating technology Walk-Over for Mud-Motor
Locating technology Wire-Line for Mud-Motor
Wire-Line drilling for Dual-Rod-Systems???
Accuracies of the different positioning/locating systems
Areas of application/application limits (drilling depth, drilling lengths, battery life)
Time required for pilot drilling
Costs for measurement technology / location technology incl. operation in comparison

## Slide 25: Session 2 – Measurement Methods/Positioning Methods in Comparison
Locating Method Walk-Over
Measurement Wire-Line for Mud-Motor
Quelle:
H.-J. Bayer, Tracto-Technik
Quelle:
iMAr Navigation GmbH

## Slide 26: Session 2 – Measurement Methods/Positioning Methods in Comparison
Locating Methods Walk-Over for Dual-Rod-System
  All companies in the field of small
  use drilling technology Walk-Over successfully
  Drilling with Wire-Line
  is currently not possible
  With Walk-Over jobs can be
  executed with good precision
Precision landing after 200 m in the Black Forest in sandstone and with 160 m
altitude difference, 18 t drilling rig
Quelle:
LEONHARD WEISS

## Slide 27: Session 2 – Measurement Methods/Positioning Methods in Comparison
Locating Methods Walk-Over for Mud-Motors
  Has been practiced in small scale drilling technology
  for years
  Many drilling companies/rig operators have never
  drilled with Mud-Motors
  Location of bit not equal to location of the
  located transmitter because there is greater distance
  between bits and transmitter (sometimes 4-5m,
  depending on the system)
  Increased "calculation effort" for the Drill master
  to pass on control commands
Quelle:
LEONHARD WEISS

## Slide 28: Session 2 – Measurement Methods/Positioning Methods in Comparison
Measurement Methods/Locating Methods Wire-Line for Mud-Motors (here Gyro)
  Common combination in large-scale HDD
  In small drilling technology < 40 t, gyros were often too "big" because necessary torques in rock could not be achieved for the required bits
  -> slimmer gyros have been designed that can
  also be used for drilling rigs < 40 t
  Some drilling companies drill with "slimmer" gyros regularly
Quelle:
LEONHARD WEISS

## Slide 29: Session 2 – Measurement Methods/Positioning Methods in Comparison
Cable-guided/Wire-Line drilling for Dual-Rod-Systems?
Quelle:
Ditch Witch

## Slide 30: Session 2 – Measurement Methods/Positioning Methods in Comparison
Accuracies of the different positioning systems
Walk-Over
  According to the manufacturer, locating technology 5 %, but empirical values are more likely to be about 2-3 % of the cover as a deviation in all directions In the case of active or passive disturbances, however, significantly higher deviations or locating is not possible at all Deviations also depend on the human factor / experience
Wire-Line (Gyro)
  Measurement engineer necessary Measurement methods should be combined with positioning methods Deviations usually low and continuous monitoring of target/actual deviations Accuracy azimuth 0.1°, inclination angle 0.05°, roll angle 0.5°, 0.1% of drilling length

## Slide 31: Session 2 – Measurement Methods/Positioning Methods in Comparison
Areas of application/application limits (drilling depth, drilling lengths, battery life)
Walk-Over
  Drilling depth limited due to signal strengths; at max. 15m – 20m (30m with depth probe) depending on geology and electromagnetic interference fields (active and passive) Danger of low battery power with too long drilling time - > longer drilling lengths sometimes critical
Wire-Line (Gyro)
  Measuring method virtually independent of the laying depth and independent of magnetic influences Power supply via cable - > longer drilling lengths no problem (cf. battery life walk-over) Risk of faulty cable connections or cable breaks

## Slide 32: Session 2 – Measurement Methods/Positioning Methods in Comparison
Time required for pilot drilling
Dual-Rod-System with Walk-Over:
Screwing/connecting inner and outer rods
Mud-Motor with Wire-Line (Gyro):
Cable connection 2-3 min
Small advantage for double drill pipe system !

## Slide 33: Session 2 – Measurement Methods/Positioning Methods in Comparison
Costs for measurement technology/location technology incl. operation in comparison
Dual-Rod-System with Walk-Over:
    Low cost of measurement
Mud-Motor with Wire-Line (Gyro):
High cost of measurement
-> approx. 3.000 €/d - 4.000 €/d additional
Clear advantage for walk-over or double rod system !

## Slide 34: Session 2 – Measurement Methods/Positioning Methods in Comparison
Advantages/disadvantages of Walk-Over compared to Gyro
 | Walk-Over Procedure | Wire-Line Procedure with opt. Gyro
Advantages: | Low costs | independent of drilling depth
 | Fast measurement | Good radius monitoring
 | No cable required | Very accurate angle measurement
 | Robust systems | No magn. Interference
 |  | Pressure measurement possible
 |  | Long drilling lengths possible
Disadvantages: | lower accuracy | only calculated positions
 | Limited drilling depth | High costs
 | Limited drilling lengths (battery life) | Wireline necessary in drill pipe
 | No monitoring of radii | sensitives Messsystem
 | mag. Interference high | 

## Slide 35: Session 3 – Drilling Fluid and Downhole Hydraulics
Water Demand / Suspension Requirements, Pumping Rates Pump Requirements per System Water availability and environmental regulations Borehole cleaning (cutting beds, washouts in the borehole due to high pressures or speeds) Flushing pressures of both systems Probability of mud break-outs Comparison of the costs for suspension requirements Comparison of wear costs on tools

## Slide 36: Session 3 – Drilling Fluid and Downhole Hydraulics
Water Demand / Flushing Requirements, Pumping Rates (Pilot Drilling)
Dual-Rod-Systems
  18 t Class 60-100 l/min
  30 t Class 60-120 l/min
  54 t Class 120-150 l/min
Mud-Motors
  18 t Class 250-300 l/min
  30 t Class 300-500 l/min
  54 t Class 500-1000 l/min
Significant advantage for Dual-Rod-System !

## Slide 37: Session 3 – Drilling Fluid and Downhole Hydraulics
Pump Requirements per System, reaming (change system pilot reaming??)
Dual-Rod-Systems
  18 t Class 60-100 l/min
  30 t Class 60-120 l/min
  54 t Class 120-150 l/min
Mud-Motors
  18 t Class 250-300 l/min
  30 t Class 300-500 l/min
  54 t Class 500-1000 l/min
Smaller pumps necessary for pilot drilling!
BUT: No difference while reaming !!
Same pumps needed for pilot drilling and reaming!

## Slide 38: Session 3 – Drilling Fluid and Downhole Hydraulics
Water availability and environmental regulations
The amount of water allowed to take from the public network or a river/stream may be limited, due to:
  Possible overloading of the water supply network Environmental regulations that limit water abstraction, esp. in summer
Clear advantage with lower suspension requirements for pilot drilling !
BUT: During reaming process, the need for flushing is higher again and there is no difference between the two systems !!

## Slide 39: Session 3 – Drilling Fluid and Downhole Hydraulics
Borehole cleaning (Cutting-Beds, Washout in the borehole due to high pressures or velocities)
  Cleaning the bottom of the borehole
Dual-Rod-Systems
Mud-Motors
Better discharge/cleaning and less
Cutting-Beds with higher flushing quantity (-speed) so advantage for Mud-Motors !
But: Risk of washout in the borehole due to high volumes!? Discussion

## Slide 40: Session 3 – Drilling Fluid and Downhole Hydraulics
Annular Mud pressures of both systems
Dual-Rod-Systems
  Usual pressures: ________ bar
Mud-Motors
  Usual pressures: ________ bar
  (Measuring annular pressure not possible with Dual rod system)
Significantly higher pressures at higher pumping rates at Mud-Motor drilling!

## Slide 41: Session 3 – Drilling Fluid and Downhole Hydraulics
Probability of mud break outs
Dual-Rod-Systems
Mud-Motors
Due to higher pressures and pumping rates, there is also a higher risk of Mud-Motor drilling for mud breakouts/Inadvertent returns!
(measuring annular pressure and better hole cleaning may result in lower risk)

## Slide 42: Session 3 – Drilling Fluid and Downhole Hydraulics
Comparison of the costs for drilling fluid
Dual-Rod-Systems
Mud-Motors
  Key Types of Costs
    Water supply (transport costs)
    Drilling fluid products (bentonites, polymers)
    Drilling fluid separation/treatment costs (personnel, equipment)
    Transport/Disposal costs (120-200 EUR/m3)
  Again! The cost advantage only applies to the pilot drilling! And if no recycling is used
Dual-Rod-Systems advantage, because significantly less flushing is needed for the pilot drilling !

## Slide 43: Session 3 – Drilling Fluid and Downhole Hydraulics
Comparison of wear costs on tools
Dual-Rod-Systems
Mud-Motors
Mud-Motors advantageous because significantly more flushing is used in the pilot drilling, which significantly reduces wear on tools and rods!
  Again! The cost advantage only applies to the pilot drilling!

## Slide 44: Session 4 – Comparison Table/Distinction Matrix and project examples
Comparison Table/Distinction Matrix project examples

## Slide 45: Session 4 – Comparison Table/Distinction Matrix
Criterion | Subsoil | Subsoil | Subsoil | Drilling Length | Drilling depths | Drilling radii
 | Rock, |  |  | [m] | [m] | [m]
 | changeable | Fels, homogen | Blocks, stones, Molar dense |  |  | 
System | with bind. Zon. |  | stored |  |  | 
Influencing factor | Geomet. BHA | Geomet. BHA | Geomet. BHA | System | Measurement | Geomet. BHA
Mud-Motor |  |  |  |  | with Gyro! | 
18 t | ++ | ++ | -- | 200-300 | without limit | 80
30 t | ++ | ++ | -- | 300-400 | without limit | 100
54 t | ++ | ++ | -- | 400-600 | without limit | 130
Doppelbohrgestänge/ |  |  |  |  |  | 
Dual Rod |  |  |  |  |  | 
18 t | ++ | ++ | - | 200-300 | 15-20 (40m) | 50 (-80)
30 t | ++ | ++ | - | 300-400 | 15-20 (40m) | 65 (-80)
54 t | ++ | ++ | - | 400-600 | 15-20 (40m) | 65 (-80)
Wertungs-System: | + | suitable | ++ | Well suited |  | 
 | - | less suitable | -- | unsuitable |  | 

## Slide 46: Session 4 – Comparison Table/Distinction Matrix
Criterion | Accuracy | Controllability | Rate of penetration | Water- | Quantity | Annular Pressure
 |  |  |  | requirement | Drilling Fluid/ | 
 |  |  |  |  | Pumprates | 
System |  |  |  |  | [l/min] | 
Influencing factor | Geomet. BHA | Geomet. BHA | System | System | System | System
Mud-Motor | Wireline | Wireline |  | (at pilot drilling) |  | 
18 t | ++ | + | no difference | high | 250-300 | Normal
30 t | ++ | + | no difference | high | 300-500 | Normal
54 t | ++ | + | no difference | high | 500-1000 | Normal
Doppelbohrgestänge/ |  |  |  | (at pilot drilling) |  | 
Dual Rod |  |  |  |  |  | 
18 t | + | 0 | no difference | Low | 60-100 | Lower
30 t | + | 0 | no difference | Low | 60-120 | Lower
54 t | + | 0 | no difference | Low | 120-150 | Lower

## Slide 47: Session 4 – Comparison Table/Distinction Matrix
Criterion | Cost | Floor space | Wear |  |  | 
 | Drill String |  | Tool |  |  | 
System |  |  |  |  |  | 
Influencing factor | System Structure | Dimensions | System/Pumprate |  |  | 
Mud-Motor |  |  |  |  |  | 
18 t | less | higher | small |  |  | 
30 t | less | higher | small |  |  | 
54 t | less | higher | small |  |  | 
 |  |  | dependent on |  |  | 
Doppelbohrgestänge/ |  |  | Pumprate |  |  | 
Dual Rod |  |  |  |  |  | 
18 t | higher | less | higher |  |  | 
30 t | higher | less | higher |  |  | 
54 t | higher | less | higher |  |  | 

## Slide 48: Session 4 – project examples
Project SuedLink, Crossings Eubigheimer Tal
Contractor: LEONHARD WEISS GmbH & Co. KG

## Slide 49: Crossings Eubigheimer Valley plan view
HDD-System 30 t
2. HDD-System 28 t t
LKWs mit Mischanlage
Aufenthaltscontainer
Radbagger
Radlader
Tanks
Quelle:
Lageplan
TransnetBW/
iLF Consulting Engineers
1 x 250 mm and 2 x 315 mm PE-pipes + 50 mm or 75 mm ducts
overground power line

## Slide 50: Crossings Eubigheimer Valley cross section
HDD-System 30 t
2. HDD-System 28 t t
LKWs mit Mischanlage
Aufenthaltscontainer
Radbagger
Radlader
Tanks
Quelle:
Längsschnitt
TransnetBW/
iLF Consulting Engineers

## Slide 51: Crossings Eubigheimer Valley geology
HDD-System 30 t
2. HDD-System 28 t t
LKWs mit Mischanlage
Aufenthaltscontainer
Radbagger
Radlader
Tanks
Quelle:
Geotechnische Bericht
TransnetBW/
iLF Consulting Engineers

## Slide 52: Project SuedLink, Crossings Eubigheimer Valley
Mud separation with centrifuge
HDD-system 30 t
2. HDD-system 28 t
Trucks with mixing unit
Vacuum unit
Containers
Wheel excavator
Wheel loader
Water tanks
Quelle:
LEONHARD WEISS GmbH & Co. KG

## Slide 53: Rockmaster (double-rod) with walk-over-system
Quelle:
LEONHARD WEISS GmbH & Co. KG

## Slide 54: „New“ walk-over-system (from U.S.) in action
Quelle:
LEONHARD WEISS GmbH & Co. KG

## Slide 55: Mud separation with centrifuge
Quelle:
LEONHARD WEISS GmbH & Co. KG

## Slide 56: 2 rigs on one job site
Quelle:
LEONHARD WEISS GmbH & Co. KG
After the conversion of Dual-Rod-System to Mud-Motor,
more powerful generator sets and pumps also had to be used

## Slide 57: As-Built – Re-measurement with Gyro
Quelle:
LEONHARD WEISS GmbH & Co. KG
1. Drilling with Walk-Over, Tiefe max. 24 m
Sudden deviation from the signal the evening before by 10m !!
-> High voltage line runs parallel!

## Slide 58: As-Built – Re-surveying with Gyro
Quelle:
LEONHARD WEISS GmbH & Co. KG
2. Drilling with Walk-Over (100m) and then with Gyro (200m), Depth max.24 m

## Slide 59: As-Built – Re-surveying with Gyro
Quelle:
LEONHARD WEISS GmbH & Co. KG
3. Drilling with Gyro, depth max. 24 m

## Slide 60: As-Built – Re-surveying with Gyro
Quelle:
LEONHARD WEISS GmbH & Co. KG
Drilling at another location with walk-over, depth max. 18 m -> very "accurately" drilled despite walk-over !!

## Slide 61: Session 4 – project examples
Project „Hangbohrung 560 m“ (no customer information)
Contractor: Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH

## Slide 62: Slope drilling 560 m Ditch Witch JT 100 with walk-over location method
Quelle:
Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH
Drilling rig:
Positioning system:
Minimum design radius
deepest point of the borehole:

## Slide 63: Slope drilling 560 m Ditch Witch JT 100 with walk-over location method
Quelle:
Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH

## Slide 64: Slope drilling 560 m Ditch Witch JT 100 with walk-over location method
Quelle:
Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH

## Slide 65: Slope drilling 560 m Ditch Witch JT 100 with walk-over location method
Quelle:
Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH

## Slide 66: Slope drilling 560 m Ditch Witch JT 100 with walk-over location method
Quelle:
Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH

## Slide 67: Slope drilling 560 m Ditch Witch JT 100 with walk-over location method
Quelle:
Bohrservice Rhein-Main, Gesellschaft für Horizontalbohrungen mbH
As Built
Design

## Slide 68: Final discussion